# VOLUME 2.  AIR OPERATOR ADMINISTRATION

## Chapter 8.  FACILITIES & EQUIPMENT

8.1.	OBJECTIVE.

This chapter provides guidance for evaluating a maintenance organization facility for original certification, change in rating, or change in location or facilities. This chapter can be applied to an AOC holder or a dedicated maintenance facility

ICAO Annex 6, Part 1, states:

8.1.1    An operator shall ensure that there is provided an organization, including trained staff, workshops and other equipment and facilities, to maintain all aeroplanes in an airworthy condition when in use.

8.1.2    When the performance of the maintenance required in 8.1 is assigned, either partially or wholly, to a maintenance organization approved by the State of Registry of the aeroplane concerned, the operator's responsibility for compliance with Standards 8.2, 8.3 and 8.4, which follow, shall be modified according to the extent to which maintenance is assigned.

8.2. 	GENERAL

A. 	When determining the suitability of permanent housing for the maintenance of airframes, the inspector should consider climatic conditions. This is to determine if worker efficiency will be adversely affected by high or low temperatures, excessive dust or sand, or other conditions. The inspector should also consider the maintenance being performed to determine if work processes are affected adversely by conditions.

B. 	Because of the requirement for testing of systems on aircraft operating under IFR and other specialized services such as X-ray, magnaflux, etc., there may be a need for an AMO to have the capability to move from location to location.

(1) 	Certificate holder/applicants may move any or all of their material, equipment, and technical personnel from place to place for the purpose of performing their functions. The address shown on the maintenance organization application will be considered the station's permanent location.

(2) 	If the station wishes to establish an additional location different than that shown on the application, the applicant should apply for satellite certification. If facilities exist that the certificate holder/applicant does not want certificated as a satellite station, they must be inspected and accepted by the Director prior to being used.

C. 	Applicants for Accessory or Instrument ratings must possess the equipment and have the capability to inspect, test, and where necessary calibrate the items that will be worked on.

  - SATELLITE MAINTENANCE ORGANIZATION INSPECTIONS

- An approved maintenance organization may apply for certification of additional facilities or locations as satellites of a parent organization. This enables the parent facility to control inspection procedures at each facility and location. Each satellite must satisfy all regulatory requirements for each rating sought. A satellite facility inspection is conducted in the same manner as a maintenance organization facility inspection.

- A letter must accompany the application. This letter must:

* 	Request the application be processed

* 	Indicate when the facilities and equipment will be ready for inspection

* 	Show the certificate number of the parent station

C. 	An application for the satellite station need not be limited to the ratings held by the parent organization. The ratings sought by the satellite must be on the application.

D. 	A maintenance organization wishing to operate a satellite maintenance facility in a foreign country must apply for a foreign maintenance organization certificate, not a satellite certificate.

.

8.4  	FOREIGN MAINTENANCE ORGANIZATIONS INSPECTIONS

A. 	The supervisory or inspection personnel of a foreign maintenance organization must be able to understand the (insert national regulations) and the maintenance and service instructions of the articles to be worked on. These personnel may not be required to hold national AME licences or approvals

(1) 	If no certificate is held, determination of performance qualifications is made by using oral tests, practical tests, or any method acceptable to the Director.

(2) 	Supervisory personnel or personnel responsible for the final inspection of work on an aircraft of (insert home country name) at a foreign maintenance organization must be able to read, write, and understand (English).

B.	Although foreign maintenance organizations are not required to comply with all national regulations, foreign maintenance organizations are required to make reports and keep records in compliance with the regulations

  - CONTRACT MAINTENANCE FACILITIES

- It many be required for an applicant for a maintenance organization certificate to provide a list of maintenance functions to be performed by other persons. To ensure the original certification criteria will continue to be met, the certificate holder must submit a revised listing when changes occur. It is the inspector's responsibility to ensure that the regulations allows the work to be contracted out. This listing must be retained in the Airworthiness office files.

B. 	If work is contracted out to a non certificated person; the certificate holder/applicant is responsible for ensuring that all work is performed in accordance with regulatory requirements.

C. 	If a certificated maintenance organization intends to perform job functions that were previously contracted out, senior inspectors should plan to observe these functions during surveillance. If this requires the addition of facilities or equipment to perform these functions, they must be inspected prior to use.

  - APPROVAL PROCESS

- Receive/Review Application Documents/Inspection Procedures Manual. Review the application for accuracy and a determination of ratings or location applied for. Also determine if any maintenance functions will be contracted out.

B. 	Evaluate Housing and Facilities. Inspect the following:

- Housing and shop areas to ensure the following:

- Adequate housing includes sufficient work space for maintenance functions to be accomplished

(b) 	If requesting an airframe rating, that housing includes:

* 	Suitable permanent housing for at least one of the heaviest aircraft within the weight class of the rating being sought

* 	If climatic conditions allow, a permanent work dock that meets the requirements of the regulations

(c) 	Proper storage and protection of:

* 	Materials

* 	Parts

* 	Supplies

(d) 	Proper identification and protection of parts and subassemblies during:

* 	Disassembly

* 	Cleaning

* 	Inspection

* 	Repair

* 	Alteration

* 	Assembly

(e) 	Segregation of the following:

*	Incompatible work areas, e.g., metal shop, battery charging area, or painting area next to an assembly area

* 	Non partitioned parts cleaning areas

(f) 	Proper ventilation, lighting, and temperature and humidity for the type and complexity of work being accomplished

(2) 	Technical documents to ensure that documents:

* 	Are in compliance with the regulations

* 	Are appropriate for the maintenance to be performed

* 	Are current, accurate, and complete and in maintenance organization's possession

* 	Are easily accessible to personnel and are controlled (no unauthorized copies)

* 	Include a method to ensure revisions are made

(3) 	Equipment, tools, and test equipment, per rating sought, to ensure:

(a) 	Required types and quantities are available and under the control of the maintenance

organization

(b) 	All required items are serviceable and within calibration criteria, to include traceability to one of the following:

*  	National Standards

* 	Standard established by the item's manufacturer

* 	If foreign manufactured, the standards of the country where manufactured, if approved by the Director

- A system exists to which makes it readily apparent to the user that the item is not overdue for calibration.

- A record keeping system exists of calibration results

NOTE: 	If the maintenance organization utilizes an engine test cell, it must be correlated to the manufacturer's specifications.

C. 	Review qualified staff list. Ensure that:

(1) 	Personnel directly in charge of maintenance functions for the maintenance organization are licenced/approved in accordance with the regulations

(2) 	The certificate holder/applicant has a list of supervisory and inspection personnel that lists at least one appropriately licenced/approved mechanic in a supervisory position.

(3) 	The certificate holder/applicant's staff list includes inspectors authorized to make final airworthiness determinations

D. 	Analyze Findings. If deficiencies were found, meet with certificate holder/applicant to discuss possible corrective actions.