VOLUME 2.  AIR OPERATOR ADMINISTRATION

Chapter 11.  MAINTENANCE RECORD KEEPING

11.1	OBJECTIVE.

The chapter provides guidance for evaluating an applicant's procedures for utilizing, preserving, and retrieving the maintenance records as required by ( insert appropriate State Regulation).

ICAO Annex 6, 8.8 Records

An operator shall ensure that the following records are kept:

a)	the total time in service (hours, calendar time and cycles, as appropriate) of the aeroplane and all life limited components;

b)	the current status of compliance with all mandatory continuing airworthiness information;

c)	appropriate details of modifications and repairs to the aeroplane and its major components;

d)	the time in service (hours, calendar time and cycles, as appropriate) since last overhaul of the aeroplane or its components subject to a mandatory overhaul life;

e)	the current aeroplane inspection status such that compliance with the maintenance manual can be established; and

f)	the detailed maintenance records to show that all requirements in the maintenance manual for issuance of a maintenance release have been met.

The records listed above  a) to e) shall be kept for a period of 90 days after the end of the operating life of the unit to which they refer, and the records in  f) for a period of one year after the issuance of the maintenance release.

The records shall be transferred to the new operator in the event of any change of operator.

11.2	GENERAL.

To comply with the maintenance recording requirements of the States Aviation Regulations, the applicant's maintenance manual must identify and contain procedures to complete an applicable documents used by the applicant.

A. 	Current Airworthiness Directive Status. The applicant must keep a record showing the current status of applicable Airworthiness Directives (ADs), including the method of compliance.

(1) 	This record shall include the following:

* 	A list of ADs applicable to the aircraft

* 	The date and time in service or cycles, as applicable

* 	The method of compliance

* 	The time in service or cycles and/or date when the next action is required (if it is a recurring AD)

(2)	An acceptable method of compliance description should include one or more of the following:

* 	Reference to a specific portion of the AD

* 	A manufacturer's service bulletin, if the bulletin is referenced in the AD

* 	Another document generated by the applicant that shows compliance with the AD, such as an Engineering Order (EO) or Engineering Authorization (EA)

(3) 	When an Engineering Order/Engineering Authorization is used, the details must be retained by the applicant. If the Engineering Order/Engineering Authorization also contains the accomplishment instructions and sign-off, it must be retained indefinitely.

(4)	An applicant may apply for an alternate method of compliance for accomplishing ADs. Alternate methods of compliance must be approved by the Director and will apply only to the applicant making the application.

(5) 	The applicant's manual must have procedures to ensure compliance with new and emergency ADs within given time limits. The procedures must ensure that the individuals responsible for implementation during other than routine duty hours are notified, as necessary.

(6) 	The document that contains the current status of ADs / method of compliance may be the same as the record of AD accomplishment, although the retention requirements are different.

(a) 	The record of AD accomplishment must be retained with the aircraft indefinitely

(b) 	The AD method of compliance record will only be retained until the work is superseded/repeated or until one year after the work is performed

B.	Total Time in Service Records

(1) 	Although the NAA may not specifically call for total time in service records of engines, propellers and rotors, it should require a record of life-limited parts for these components. The only way to accomplish this is by keeping records for total time in service.

(2) 	Total time in service records may consist of aircraft maintenance record pages, separate component cards or pages, a computer list, or other methods as described in the applicant's manual.

C.	Life-Limited Parts Status Records. (Appropriate State Regulation) requires records for components of the airframe, engine, propellers, rotors, and appliances that are identified to be removed from service when the life limit has been reached.

(1)	The current life-limited status of the part is a record indicating the operating time limits, total number of hours or accumulated cycles, or the number of hours or cycles remaining before the required retirement time of the component is reached. This record must include any modification of the part in accordance with ADs, service bulletins, or product improvements by the manufacturer or applicant.

(2) 	The following are not considered a current life-limited status record:

* 	Work orders

* 	Maintenance installation records

* 	Purchase requests

* 	Sales receipts

* 	Manufacturers documentation of original certification

* 	Other historical data

(3) 	Whenever the current status of life-limited parts records cannot be established or has not been maintained (e.g., a break in current status) and the historical records are not available, the airworthiness of that product cannot be determined and therefore it must be removed from service.

D.	Airworthiness (Maintenance) Releases

(1) 	When maintenance, preventive maintenance, or modifications on an aircraft are performed, an airworthiness release or log entry must be completed prior to operating the aircraft. Using the procedures described in the manual, the applicant must be able to retain all of the records necessary to show that all requirements for the issuance of an airworthiness release have been met.

E. 	Overhaul List. The applicant is required to develop manual procedures for recording the time since the last overhaul of all items installed on the aircraft that are required to be overhauled on a specified time basis. The items requiring overhaul are listed either on the operations specifications or in a document referenced to in the operations specifications or CMM.

(1) 	The overhaul list includes the actual time or cycles in service since the last overhaul of all items installed on the aircraft. If continuity cannot be established between overhaul periods, the last overhaul records must be reviewed to reestablish the currency of the overhaul list.

(2) 	The overhaul list refers to the time since the last overhaul of an item and must not be confused with an overhaul record, which requires a description of the work and identification of the person who performed and/or approved the work.

E.	Overhaul Records

(1) 	A record must be made whenever an item of aircraft equipment is overhauled and must include the following:

* 	A description of the work performed or reference to data acceptable to the (Director)

* 	The name of the person performing the work

* 	The name or other positive identification of the individual approving the work

NOTE: A return to service tag does not constitute an overhaul record.

(2) 	The applicant must retain the record and be able to make it available to the (Director) upon demand. The overhaul records shall be retained until the work is superseded by work of equal scope and detail.

G. 	Current Aircraft Inspection Status. The applicant is required to retain a record identifying the current inspection status of each aircraft.

(1) 	This record shall show the time in service since the last inspection required by the inspection program under which the aircraft and its appliances are maintained.

(2) 	Inspection work packages or routine and nonroutine items generated while performing any part of the inspection program must be retained as follows:

* 	For one year after the work is performed

* 	Until the work is repeated or superseded by other work

H. Major modification and Major Repair. Applicants are required to retain records of current major repairs and major modifications that are accomplished on the following:

* 	Airframe

* 	Engine

* 	Propeller

* 	Rotor

* 	Appliance

(1) 	Major modifications must be listed with the date of modification and a brief description of the work accomplished. The manual must have procedures for the following:

* 	Extracting the information required for the list from the actual modification record of accomplishment

* 	For transmitting an modification report to the local CAA office

(2) 	The manual must contain procedures for retaining a report of each major repair and making it available for inspection by the CAA.

11.3 	APPROVAL PROCEDURE

A. 	Review the Applicant's Maintenance Manual

(1) 	Ensure that the necessary procedures exist in the applicant's manual to ensure a suitable system for creating, preserving and retrieving required records.

(2) 	Ensure that all records will contain the following information, as applicable:

* 	Description of the work performed (or reference to data acceptable to the (Director))

·	Name of the person(s) performing the work

·	Name or other positive identification of the individual approving the work

B. 	Review the Applicant's Manual's Procedures. Review the applicant's record keeping procedures to ensure that the requirements of (Appropriate State Regulation) are met for the following:

(1) 	Airworthiness Release Records. Ensure the following:

(a) 	Airworthiness release records will be retained for one year after the work is performed or until the work is repeated or superseded

(b) 	The applicant's manual identifies the person(s) authorized to sign an airworthiness release

(2) 	Flight Maintenance Records. Ensure that procedures provide for the following entries:

* 	Flight discrepancies to be entered at the end of each flight

* 	Corrective actions and certification, per manual procedures

* 	Certifications for Duplicate Inspection , according to manual procedures by authorized personnel

* 	Minimum Equipment List (MEL) deferment per the manual procedures

(3) 	Total Time In Service Records

(a) 	Evaluate the method of recording total time in service of airframes. This record must show the current time in service in hours.

(b) 	Ensure that procedures are in place to retain the records until the aircraft is sold and that the records will then be transferred with the aircraft.

(4) 	Life-Limited Parts Status

(a) 	Ensure that the applicant has procedures for tracking the current status of life-limited parts for each airframe, engine, propeller, rotor, and appliance, to include the following information:

* 	Total operating hours (including calendar time)/cycles accumulated

* 	Life limit (total service life)

* 	Remaining time/cycles

* 	Modifications

(b) 	Ensure that procedures are in place to retain the records until the aircraft is sold and are then transferred with the aircraft.

(5)	Time Since Last Overhaul Records. Ensure that the manual includes a method/procedure for updating this document from the overhaul records and ensuring that this document accompanies the aircraft upon sale

(6) 	Overhaul Records

(a) 	Ensure that the manual describes how the applicant will document the last complete overhaul of each airframe, engine, propeller, rotor and appliance. The overhaul record should include the following information:

* 	Disassembly data

* 	Dimensional check data

* 	Replacement parts list

* 	Repair data

* 	Reassembly/test data

* 	Reference to data including overhaul specifications

(b) 	Ensure that these records will be retained until the work is superseded by work of equivalent scope and detail.

(7) 	Current Aircraft Inspection Status

(a) 	Evaluate the method the applicant will use to record the time in service since the last inspection.

(b) 	Determine if procedures ensure that these records are retained until the aircraft is sold and are then transferred with the aircraft.

(8) 	Airworthiness Directive (AD) Compliance. Evaluate how the applicant will comply with the record keeping requirements of the ADs. The procedures must generate a record that contains the following data:

(a) 	Current status. Ensure that the current status data will include the following:

* 	A list of all ADs applicable to the aircraft

* 	The date and time of compliance

* 	The time and/or date of next required action (if a recurring AD)

(b) 	Method of compliance. Ensure that this data will include either a record of the work performed or a reference to the applicable section of the AD.

NOTE: This data must be retained until the aircraft is sold and transferred with the aircraft.

(9) 	Major modification Records

(a) 	Evaluate the manual procedures to ensure that the applicant prepares and maintains a list of current major modifications to each airframe, engine, propeller, rotor, and appliance.

(b) 	Ensure that the list includes the following information:

* 	The date of the modification

* 	A brief description of the modification

(10) 	Major Repair Records. Evaluate the manual procedures to ensure that the applicant prepares and maintains a report of all major repairs to each airframe, engine, propeller, rotor, and appliance.

11.4		ANALYZE THE FINDINGS. Evaluate all deficiencies to determine if corrective actions will   be required.