# VOLUME 2.  AIR OPERATOR ADMINISTRATION

Chapter 34.  FLIGHT PERMITS - FERRY FLIGHTS

34.1 Objective.

This chapter provides guidance for evaluating an application from an operator to allow him to authorize ferry flights. This authorization is normally granted by amending his operations specifications or CMM and Operations manual to allow for the in-house issue of a special flight permit to conduct a ferry flight.

34.2. General

- Definition: Damaged aircraft - An aircraft that has sustained physical damage or has inoperative/malfunctioning equipment.

- Issuance. The authorizing regulation of the NAA, should not automatically authorize the issuance of permits to all operators. Therefore, an eligible operator's operations specifications or Company Manuals (operations and maintenance) will be used to authorize the issue of such permits and to ensure responsible utilization of the permit.

- Eligibility

- The authority to issue special flight permits should only be given to certain operators subject to the following regulations:

- Aircraft involved in an accident or incident may not be ferried prior to notifying the CAA accident investigation coordinator.

(3) An Airworthiness Directive (AD) may dictate that safety demands further limitations. The AD may   limit ferry flights to those specifically approved by the CAA.

- No person may operate an aircraft to which an AD applies except in accordance with the requirements of that AD. Therefore, if an AD requires compliance before further flight, with no provision for the issuance of special flight permit, the operation of the specified aircraft would not be permitted.

- Manual Review

- The operator should consider certain conditions and the limitations necessary before authorizing the operation of an aircraft. These conditions and limitations should be included in the operator's manuals.

- When reviewing manual material, the following items should be considered:

(a) Technical data

(b) Operational equipment necessary for safe operation of the aircraft

(c) Aircraft weight limits

(d) Fuel distribution limits

(e) Center of gravity limits

(f) Aircraft maneuver limitations

(g) Flight equipment usage, limitations, e.g., autopilot, etc.

(h) Airspeed limits

(i) Meteorological limits, including:

* Conditions to be avoided

* Required inspections when these conditions are encountered

* Weather minimums

- Authorization for Ferry Flights with one Engine Inoperative.

Certain large transport category aircraft operators may be authorized to conduct a ferry flight of a four engine airplane or a turbine engine powered airplane equipped with three engines, with one engine inoperative, to a base for the purpose of repairing that engine. The following restrictions should apply:

(1) 	The particular airplane model must have had a test flight conducted with an engine inoperative in accordance with performance data contained in the applicable airplane flight manual

(2) 	The approved airplane flight manual must contain the performance data

(3)	 The operator's manual must contain operating procedures for the safe operation of the airplane, including the specific requirements listed in the appropriate regulation

(4) 	The operator may not depart an airport where the initial climb-out is in thickly populated or the weather conditions at the takeoff or destination airport are less than those required for Visual Flight Rules (VFR) flight

(5) 	Only required flight crewmembers can be carried aboard during this ferry flight

(6) 	The required flight crewmembers must be trained, and be thoroughly familiar with the company's operating procedures and the airplane Approved Flight Manual, for one-engine inoperative ferry flights.

34.3 APPLICATIONS INVOLVING FOREIGN AIR TRANSPORTATION.

ICAO Annex 8 recognizes the temporary loss of airworthiness due to damage to the aircraft. In this case, damaged aircraft can refer to inoperative or malfunctioning equipment as well as physical damage to the aircraft. In such an event, Annex 8,Part II, Section 6.2.2, recognizes that the country of registry may allow the aircraft to be ferried to a where it can be restored to an airworthy condition.

Since Annex 8 provides for this flight situation, an operator is not required to obtain permission to fly over, into, or out of foreign countries when exercising the provision of a special flight permit for purposes of repair.

NOTE: This authorization does not extend to situations, which involve flying an undamaged aircraft to a base where modifications will be performed.

34.4. DISPLAY OF PERMIT.

The operator must display in the aircraft the current airworthiness certificate, including the special flight permit or authorization. The operator must carry on board the aircraft a copy of those conditions and limitations imposed by the Director and contained in the operations specifications or company manual.

34.6. PROCEDURES

A. Review the Operator's Operations and Maintenance Manuals

(1) Ensure that the manuals have the following procedures for ferry flights:

(a) Provisions for conveying the authorization to the operating crew

(b) A system for recording details of each flight conducted under this authorization

(c) Procedures to determine that the proposed special flight complies with the (insert country name ) Regulations and is not prohibited by any Airworthiness Directives (ADs)

(d) Procedures to allow additional crewmembers and other authorized persons to be carried aboard the aircraft during ferry flights when the aircraft flight characteristics have not been appreciably changed or its operation in flight has not been substantially affected

(e) Procedures to ensure the display of the current airworthiness certificate and the special flight permit or authorization

(f) Procedures to ensure the review of the following items prior to releasing the ferry flight:

- Technical data to which the aircraft must perform

- Operational equipment necessary for safe operation of the aircraft

- Aircraft weight limits

- Fuel distribution limits

- Center of gravity limits

- Aircraft maneuver limitations

- Equipment usage limitations, e.g., autopilot

- Airspeed limits

- Meteorological limits, including conditions to be avoided, inspections required should these conditions be encountered inadvertently, and weather minimums

(g) Procedures to ensure that such flights are only approved by senior operations and airworthiness management staff.

(2) For one engine inoperative ferry flights, ensure the following:

(a) The operator has a four engine airplane or a turbine engine powered airplane equipped with three engines

(b) The applicable airplane has been previously test flown with one engine inoperative in accordance with its approved Airplane Flight Manual. The approved Airplane Flight Manual must contain the following data:

- Maximum weight

- Configuration of the inoperative propeller, if applicable

- Runway length for takeoff, including temperature accountability

- itude range

- Certificate limitations

- Ranges of operational limits

- performance information

- Operating procedures

(3) The operator's manual must include the following:

- A limitation that the operating weight on any ferry flight must be the minimum necessary with the necessary reserve fuel load

- A limitation that takeoffs must be made from dry runways unless, based on a showing of actual runway operating takeoff techniques on wet runways with one engine inoperative, takeoffs with full controllability from wet runways have been approved for the specific model aircraft and included in the approved Airplane Flight Manual

- Procedures for operations from airports in which the runways may require a takeoff or approach over populated areas

- Inspection procedures for determining the operating conditions of the operative engines

- A restriction that no person may takeoff from an airport in which the initial climb is over thickly populated areas or weather conditions at the takeoff and destination airport are less than those required for Visual Flight Rules (VFR) flight

- Procedures that ensure carrying only essential flight crewmembers aboard the airplane during the ferry flight

- Procedures that ensure flight crewmembers are thoroughly familiar with the operator's operating procedures and the approved Airplane Flight Manual for one engine inoperative ferry flights

B. Ensure that the CAA Accident Investigator is advised prior to any authorization of an aircraft involved in an accident or incident