# VOLUME 2.  AIR OPERATOR ADMINISTRATION

# CHAPTER 39. SPECIAL CERTIFICATES OF AIRWORTHINESS -      OVERVIEW

## 39.1	OBJECTIVE

This chapter provides guidance and information relating to the issue of special Certificates of Airworthiness (CoAs) in particular categories.

## 39.2.	BACKGROUND

Aircraft airworthiness certification is the whole process of assessing an aircraft type against its type design and the aircraft’s condition for safe operation, which culminates in issue of Certificates of Airworthiness (CoA) for individual aircraft. Type Certification is a part-process of aircraft airworthiness certification which leads to issue of a Type Certificate or equivalent document. This is necessary before an individual CoA can be issued for most categories of aircraft

The obligation for Contracting States of the International Civil Aviation Organisation (ICAO), is to issue CoAs, is laid down in Part II, Section 3 of ICAO Annex 8, “Airworthiness of Aircraft”. A CoA may be issued on the basis of satisfactory evidence that an individual aircraft has been constructed and assembled satisfactorily. The airworthiness categories in which CoAs may be issued are described in detail in Chapter 37 “Aircraft Airworthiness Certification Categories and Designations Explained”

CoAs are issued for every individual Aircraft registered in this state as one of the pre-conditions to them being able to fly legally, in the sense of being fit to fly. Actual aircraft type approval stops at the issue of the Type Certificate. However, before the first of a type can actually fly in this state, a CoA must be issued.

Certification of individual standard category aircraft (the CoA issue process) involves:

(a)	ensuring that the aircraft conforms with the definition of the design and its method of construction i.e. the aircraft conforms to the type design; this in turn ensures that the aircraft meets (i) a design standard and (ii) the specified airworthiness requirements;

(b)	ensuring that the aircraft is free from manufacturing and post-production test defects;

(c)	ensuring that the required modifications, as dictated by both design changes and specific national Airworthiness Directives (ADs), have been embodied;

- ensuring that the required operational equipment has been fitted; and

- ensuring that the aircraft’s airworthiness state is properly reflected in the required documentation.

If these conditions are met, then the aircraft can be issued with standard CoA in particular categories. Full information is contained in chapter 38, “Standard Certificates of Airworthiness.”

Special CoAs are issued to aircraft which do not meet the requirements of the Civil

Aviation Regulations.  Note that an aircraft must not be operated on a special CoA in international airspace or in the territory of a foreign country without the specific permission of that country.

## 39.3.	SPECIAL CERTIFICATES OF AIRWORTHINESS

The following categories of aircraft are issued with special CoAs:

Primary

Restricted

Limited

Amateur Built (Accepted under the control of a EAA type organisation)

The following are designated special CoA:

Provisional CoA

Experimental certificate

Special flight permits

## 39.4 APPLYING FOR A SPECIAL CERTIFICATE oF AIRWORTHINESS

### 39.4.1	Who may apply

The regulations normally state that “the holder of the Certificate of Registration (CoR) is eligible to apply for a CoA for the aircraft”

Therefore one major prerequisite for application for a CoA is that the aircraft must already be registered on this states Civil Aircraft Register.